## Slide 1
Kyung Min Kim
E-mail: kyoungmin2@naver.com
SoC & Microprocessor Research Laboratory
Single-Cycle ARM Processor Design
1st Term Project

## Slide 2: Flow
Instruction Analysis
Control Signal Analysis
Module Implementation
1st Term Project
2nd Term Project

## Slide 3: Single-Cycle ARM Processor

## Slide 4: Altera DE2 FPGA Board

## Slide 5: 1st Term Project
Given processor is able to run following instructions
  Branch : B, BL
  Arithmetic : ADD, SUB, CMP, MOV
  Load/Store : LDR, STR
Given processor is able to run following suffixes
  Logical : EQ, NE
Addressing Modes
  Addressing Mode 1 : 1 (immediate), 2 (register)
  Addressing Mode 2 : 1 (immediate offset), 2 (register offset)

## Slide 6: inst_data.mif
address
(HEX)
instruction
(HEX)
EA000006

## Slide 7: arm_architecture_reference_manual.pdf
Read ‘Chapter A3 The ARM Instruction Set’ (pp. 109) and ‘Chapter A4 ARM Instructions’ (pp. 151)

## Slide 8: Program Status Registers
Condition code flags
  N = Negative result from ALU
  Z = Zero result from ALU
  C = ALU operation Carried out
  V = ALU operation oVerflowed
If S bit is 1, update NZCV flags according to result from ALU

## Slide 9: Condition code flags
Cond | Mnemonic | Meaning | Condition flag state
0000 | EQ | Equal | Z = 1 (Zero is set)
0001 | NE | Not Equal | Z = 0 (Zero is clear)
1110 | AL | Always | 
ARM Example
  CMP r0, #5 // cond = 1110, (r0 == #5) ? Z = 1 : Z = 0
  BEQ Bypass // cond = 0001
  ADD r1, r1, r0
  SUB r1, r1, r2
  Bypass …
MIPS Example
  beq $s3, $s4, True // Branch if $S3 == $4
  sub $s0, $s1, $s2
  j Exit
  True: …
  Exit: …

## Slide 10: Example
EA000006
  Convert hexadecimal to binary
    1110 1010 0000 0000 0000 0000 0000 0110 (2)
  Describe which instruction is through ‘arm_architecture_reference_manual.pdf’
    B #6;
  Describe what instruction means
    Move to PC + 8 + 6x4 address (note that this is +4 for MIPS)
    Go to address 008
      The next instruction becomes ‘E59F2EC8’ at address 008

## Slide 11: Example
E59FDE78
  Convert hexadecimal to binary
    1110 0101 1001 1111 1101 1110 0111 1000 (2)
  Describe which instruction is through ‘arm_architecture_reference_manual.pdf’
    LDR $13, [$15, #0xE78];
    Since the 25th bit I bit is 0, it is indicated by #
  Describe what instruction means
    Read the value from the memory of the address added by the value of register 15 and the value of # 0xE78 and store it in register 13

## Slide 12: Example
E1A0F00E
  Convert hexadecimal to binary
    1110 0001 1010 0000 1111 0000 0000 1110 (2)
  Describe which instruction is through ‘arm_architecture_reference_manual.pdf’
    MOV $15, $14;
  Describe what instruction means
    Store the value of register 14 in register 15

## Slide 13: 1st Term Project
5 points (2nd term project is 25 points)
What to submit
  Analyze instructions from 000 to 024 in order of operation
    Convert hexadecimal to binary (0.5 points)
    Describe which instruction is through ‘arm_architecture_reference_manual.pdf’
    (0.5 points)
    Describe what instruction means (4 points)
How to submit
  Send a report file to kyoungmin2@naver.com
    Due date: 10/31 23:59
    Both Korean and English are available
    Please fill in the fille name as ‘StudentNumber_Name_1stTermProject’
      Ex) 2018010594_김경민_1stTermProject.docx

## Slide 14
Q&A