## Slide 1
Kyung Min Kim
E-mail: kyoungmin2@naver.com
SoC & Microprocessor Research Laboratory
Single-Cycle ARM Processor Design
2nd Term Project

## Slide 2: FPGA vs ASIC
Reference: https://anysilicon.com/fpga-vs-asic-choose/

## Slide 3: Design Flow
Functional Specification
HDL
Synthesis
Place & Route
Download and Verify in Circuit
Behavioral Simulation
Static Timing Analysis
Functional Specification
HDL
Synthesis
Place & Route
Verify in Circuit
Behavioral Simulation
Static Timing Analysis
Equivalency Checking
Static Timing Analysis
Equivalency Checking
Verification of 2nd & 3rd Order Effects
FPGA
ASIC

## Slide 4: Synthesis and Place & Route (FPGA)
Synthesis: The process of making a circuit written in Verilog HDL or VHDL into a netlist of logic gates
Place & Route: As implied by the name, it is composed of two steps, placement and routing. The first step, placement, involves deciding where to place all electronic components, circuitry, and logic elements in a generally limited amount of space. This is followed by routing, which decides the exact design of all the wires needed to connect the placed components. This step must implement all the desired connections while following the rules and limitations of the manufacturing process.
HDL
Netlist of Logic Gates
Synthesis
P & R
Place
Route

## Slide 5: Overview
Instruction Analysis
Control Signal Analysis
Module Implementation
1st Term Project
2nd Term Project

## Slide 6: Overview

## Slide 7: Overview
Given processor is able to run following instructions
  Branch : B, BL
  Arithmetic : ADD, SUB, CMP, MOV
  Load/Store : LDR, STR
Given processor is able to run following suffixes
  Logical : EQ, NE (‘Z’ in ‘NZCV’)
Addressing Modes
  Addressing Mode 1 : 1 (immediate), 2 (register)
  Addressing Mode 2 : 1 (immediate offset), 2 (register offset)

## Slide 8: Overview
1) Instruction fetch (Clock 0’s posedge)
2) Check condition code & Initialize control signal
3) Register read (Clock 90’s posedge)
4) ALU
After ALU operation: Update NZCV
5) Memory read / write (Clock 0’s negedge)
6) Register write (Clock 90’s negedge)
1)
Clock 0: blue, Clock 90: red
2)
3)
4)
5)
6)
(Clock 0 and Clock 90 connected memory and register, in respectively)
1 Clock Cycle
Clock

## Slide 9: Module
ARMProcessor module
  Input
    clk : Clock 90
    reset : reset if press return button
    inst[31:0] : current instruction
    readdata : data from memory
  Output
    pc : instruction address (starting at 0)
    be[3:0] : 1111(2) (default) – don’t change!
    memaddr[31:0] : data address
    memread : 1(2) (default) – don’t change!
    memwrite : specify whether memory is to be written
    writedata[31:0] : write data to memory

## Slide 10: Module
RegisterFile Module
  Register 14 ($14) – Link Register (LR)
    This register holds the address of the next instruction after a Branch and Link instruction
    $14 = PC + 4
  Register 15 ($15)
    It can be used in most instructions as a pointer to the instruction which is two instructions after the instruction being executed
    $15 = PC + 8
PC (It is different with Register 15($15))
  PC (next instruction) = PC (current instruction) + 4

## Slide 11: Module
Extend Module
  Data Processing Type: zero extended-imm8
    0000/1010(2) -> 0000/0000/0000/0000/0000/0000/0000/1010(2)
  Load/Store Type: zero extended-imm12
    0000/1010/0000(2) -> 0000/0000/0000/0000/0000/0000/1010/0000(2)
  Branch Type: sign-extended-imm24, shifting left two bits
    1000/0000/0000/0000/1010/0000(2) -> 1111/1110/0000/0000/0000/0010/1000/0000(2)
    0000/0000/0000/0000/1010/0000(2) -> 0000/0000/0000/0000/0000/0010/1000/0000(2)

## Slide 12: Control signal
RegSrc
  RegSrc[0] = “0” : ADD, SUB, CMP, MOV, LDR, STR
    Using Register[inst(19:16)]
  RegSrc[0] = “1” : B, BL
    Using Register[15] for calculating branch target address

## Slide 13
Tutorial 1
Programming the DE2 board
http://youtu.be/bg3h7uU_p6U

## Slide 14: Tutorial 1
Install Quartus2 9.1sp2 Web Edition
  Official Website: https://www.altera.com/downloads/software/quartus-ii-we/91sp2.html
  Google Drive: https://drive.google.com/open?id=1fmDbWMtaFuT1wJu_11-Jd31gp3Rsm1gp

## Slide 15: Tutorial 1
How to use

## Slide 16: Tutorial 1
How to use

## Slide 17: Tutorial 1
How to use
  You need to set the device number of the board you have received
    Please check the device number because devices can have different numbers

## Slide 18: Tutorial 1
How to use
  File  New  Verilog HDL File  OK

## Slide 19: Tutorial 1
How to use
Same to project name!!
Start Compilation

## Slide 20: Tutorial 1
How to use
  Assignments  Pin Planner  View -> All pins list -> “Fill in the Location”  “Close Pin Planner”  Start compilation
Refer to the attached file “DE2_Pin_Table”

## Slide 21: Tutorial 1
How to use
Button
Power USB

## Slide 22: Tutorial 1
Install Driver (Windows 7/8)
  “Connect USB & Turn on FPGA“  장치 관리자  “Right click on USB-Blaster”  Install driver software

## Slide 23: Tutorial 1
Install Driver (Windows 7/8)
  “Click Browse”  <Path to Quartus installation>/drivers/usb-blaster directory

## Slide 24: Tutorial 1
How to use
  Tools  Programmer

## Slide 25: Tutorial 1
How to use
  Tools  Programmer

## Slide 26: Tutorial 1
How to use
  Tools  Programmer

## Slide 27: Tutorial 1
How to use

## Slide 28: Tutorial 1
How to use
  If you do not see the light when you turn up the two switches as shown in the picture below, please send an e-mail to TA (kyoungmin2@naver.com) until 11/4

## Slide 29
Tutorial 2
Timing Simulation

## Slide 30: Tutorial 2

## Slide 31: Tutorial 2
1
2
3
Click !
Click !
Click !

## Slide 32: Tutorial 2
1
2
Right Click !
Click !

## Slide 33: Tutorial 2
Check !

## Slide 34: Tutorial 2
2
1
Click !
Click !

## Slide 35: Tutorial 2
Click !

## Slide 36: Tutorial 2
Check !
Click !

## Slide 37: Tutorial 2
Timing Simulation Result

## Slide 38: Tutorial 2
Click !

## Slide 39: Tutorial 2
Right Click !
Click !

## Slide 40: Tutorial 2
Click !

## Slide 41: Tutorial 2
Click !

## Slide 42: Tutorial 2
Click !

## Slide 43: Tutorial 2
Click !

## Slide 44: Tutorial 2
Select the radix
Click !

## Slide 45: Tutorial 2
Success

## Slide 46
Tutorial 3
2nd Term Project

## Slide 47: Tutorial 3
CA_2018_2_term -> ARM_System_Syn -> ARM_System.qpf
  Coding 5 modules (‘RegisterFile.v’, ‘ControlUnit.v’, ‘Extend.v’, ‘ALU.v’, ‘ARMProcessor.v’) using Verilog HDL
Don’t change!!!
Our project

## Slide 48: Overview
ARMProcessor.v
ControlUnit.v
RegisterFile.v
Extend.v
ALU.v

## Slide 49: Tutorial 3
ARMProcessor.v
Don’t remove!!!
(But you can add something for timing simulation)
Your Code

## Slide 50: 2nd Term Project
What to submit (Total 25 points)
  Project folder
    RegisterFile.v (2 points)
    ControlUnit.v (2 points)
    Extend.v (2 points)
    ALU.v (2 points)
    ARMProcessor.v (15 points)
      15 points will be given depending on whether the top module operates or not
  Report (2 points)
    Module description
    If the timing simulation does not work on the board even though it works properly, please capture the timing simulation result and write it in the report
How to submit
  Send a report file to kyoungmin2@naver.com
    Due date: 12/6 23:59
    Both Korean and English are available
    Please fill in the fille name as ‘StudentNumber_Name_2ndTermProject’
      Ex) 2018010594_김경민_2ndTermProject.zip

## Slide 51
Q&A